Instructions based on Aerotech RMS 24/40, and E18-4W reloads
6/22/2014 DK

1. Push in Main charge assembly and center in Metal tube

2. Partially screw in Delay assembly (grease threads)

3. Partially screw in Yellow metal retainer (grease threads)

4. Screw Delay assembly all the way in

5. Screw Yellow metal retainer all the way in.

Whole engine assembly

Big fat o-ring

Big skinny o-ring

Washer

Delay Assembly

Main charge assembly

>When assembling engine, lightly grease o-rings and threads

>Underline parts are your reusable 24/40 parts.

>All diagrams have the same Aft to Forward perspective.

Spacer (if provided)

Scotch tape, square piece

Charge (with slot)

Tube

Push the Tube, Charge, Scotch tape, and Spacer together until flush with Aft end. Once the engine is together, the Scotch tape will act as a stop to properly position the igniter.

Big skinny o-ring

Big fat o-ring

Small fat o-ring

Aft (fire+thrust)         Forward (parachute)

Delay charge tube

Spacer (if provided)

Delay charge

Small fat o-ring

Metal delay assembly housing

Metal tube

Single use metal nozzle

Yellow metal retainer

Main charge assembly

Delay assembly